Architecture Coursework

1i) By adding IR6-15 to the inputs to M2 and adding another control signal C5, also to M2, the two control signals C2 and C5 to select which inputs to use for the Register File. This would look like the following:

therefore the outputs from M2 would be based on the C2 and C5 would be the following:

C2	C5	M2 Output
0	0	MDR output
0	1	IR6-15
1	0	Aout output
1	1	unused

The registers and control signals that would be used in the LOADI instruction are:
Step 1:
PCwrite:
C1:
Mread:
IRwrite:
IR:

Step 2:
C2:
C5:
IRwrite:

iii) the new state diagram, after these alterations, would look as such:

Mread
IR Write
PC Write
C1=1, C3 = 0
0

1
4

2
5

PCwrite
C3 = 1
C4 = 1
Mread
MDR
C1=0
Rwrite
C2 = 0
C5 = 1
Mread
MDR write

3
6

Rread
A1 write
A2 write
Rwrite
C2 = 0

7

Aout Write
ALU control = 0

8

Rwrite
C2 = 1

2i) The “+1” unit can be remove by adding 2 new multiplexers, say M4 and M5, which lead into the ALU, into M4 would lead the PC output and the output of the A1 register and into M5 would be an input which was fixed as one, this is hard coded, and the output from the A2 register. Both of these new multiplexers would use a single control signal C6 which would determine whether to use the PC output and the 1 input or A1 and A2 outputs. The output from the ALU would then go into the Aout register and then the output from this register into M3. If we wish to then increment the PC, we do this by setting C6 to 0, so the ALU inputs are 1 and the current PC value, and using the ALU control signal so it adds the values together, STUFF GOES HERE ABOUT C4 AND C3 AND PC WRITE, so the output from M3 into the PC is the original PC value +1. The following set-up would look as such:

CHANGE THE IMAGE