The Challenges of Parallel Programming

Parallel Overhead
Due to the complex nature of making a program parallel, it takes time to coordinate these	parallel tasks, time that could be used to perform useful tasks, the parallel overhead is this	time. This includes:
- the time to start/terminate a task
- the time to pass messages bewtween task
- sychronization times
- etx.
This time is unavoidable but must considered when parallel computing is to be used[1]

Sychronization

Sychronisation is a necessary consideration when using multiple threads to avoid race	conditions. This limits the parallel effieceny of the program. If this is done incorrectly than	we obtain incorrect results from the program, as there may be errors in the access of shared	resources.[1]

Scalability

Amdahl's Law

Amdahl's Law is a model for the relationship between the expected speedup of parallel	implementations of an algorithm, relative to the serial algorithm, if we assume that the	problem size remains constant. This concerns the speedup achievable from some	improvement to a computation that affects a proportion P of that computation, with a	speedup of S. The law states:

it is clear to see that if we consider the imporvement to be the parallisation this can be used	to model the speedup achievable by making the portion, P, of the program parallel instead of
serial. Thus it is clear to see that we are limited by how much we can improve a program
by making it parrallel, and it is heavily influenced by how much of the program can be made	parallel.[2]
Load Balance[1][3]
This is important in threaded applications so that we fully utilize available processors. Once
a task has finished its job on the processor, it remains idle until new tasks are assigned to it.
To achieve optimal performance results we must equally partition the work each task	receives, such as evenly distributing loop iterations across the tasks. Using dynamic work
assignments, when the amount of work each task will perform is intentionally variable or	unpredictable, we may need some sort of scheduler, so that as it task finishes a new one is	set.

Granularity[1]

Communications

Latency vs. Bandwith

The latency is the time it takes to send a minimal message from a point A to a second, B.
e.g. microseconds. The bandwidth is the amount of data that can be communicated per unit	time. e.g. megabytes/sec. If many small messages are sent this can cause latency to	dominate communication overheads. It is, often, more efficient to bundle these messages	together into a larger message as this increases the effective communications bandwidth.[3]

Synchronus vs. asynchronous communications[3]

[1] - http://www.intel.com/technology/itj/2007/v11i4/3-development/4-challenges.htm
[2] - http://www.princeton.edu/~achaney/tmve/wiki100k/docs/Amdahl_s_law.html
[3] - https://computing.llnl.gov/tutorials/parallel_comp/#DesignCommunications